## Slide 1
VK26-IITI-AHM-0295

## Slide 2
Project Overview
Title - ‘SwasthEdge’
Team ID - VK26-IITI-AHM-0295
Track - Theme: Al in Hardware Manufacturing
Sub-Theme: Edge Al & On-Chip Processing
“A low-cost self-diagnosing edge controller that fuses sensor, electrical, and controller-health data to confirm faults locally and trigger appropriate responses without continuous cloud connectivity.”

## Slide 3
Problem Statement
Operational Pain Point -
          Low-cost edge controllers in industrial and remote environments can face sensor drift, disconnection, abnormal power consumption, and supply instability, creating a need for an embedded system that can monitor device and sensor health, distinguish persistent faults from temporary abnormalities, and provide an appropriate local response.
Target Beneficiary Segment -
Small and medium-scale industries, manufacturing systems, smart agriculture, environmental monitoring, remote infrastructure, and Industrial IoT/edge deployments where continuous network connectivity or manual monitoring may not always be available.

## Slide 4
User Journey – Before State
Flowchart
Operational Impact
Incorrect operation
Equipment damage
Unplanned downtime
Maintenance risk
Fault-Detection Latency | False-Alarm Behaviour | Processing Overhead | Operational Impact
Time taken to recognize an injected fault | Incorrect responses to temporary abnormalities | CPU / RAM / processing cost | Effect of undetected or delayed faults
Baseline values will be established through controlled fault-injection tests before SwasthEdge evaluation.
BASELINE INEFFICIENCY — TO BE ESTABLISHED
Existing Edge System
Sensor / Device Abnormality Occurs
Abnormality Is Difficult to Interpret
Fault May Remain Undetected

## Slide 5
Flowchart
SwasthEdge Retrofit
Continuous Health Monitoring
Appropriate Local Response
Local Diagnostic Logging
Operational Benefit
Safer operation
Reduced Maintenance risk
Reduced downtime
Early fault awareness
From reactive detection to locally confirmed, self-diagnosing operation
Fault-Detection Latency | Fault-Confirmation | Processing & Power Overhead | Local Response & Continuity
Time from fault injection to local detection | Ability to distinguish persistent faults from temporary abnormalities | CPU / RAM / processing latency / additional power | Response state and diagnostic retention during network loss
SwasthEdge performance will be compared with sensor-only detection using controlled fault-injection tests.
EFFICIENCY METRICS — TO BE BENCHMARKED
User Journey – After State
Fault Detection & Analysis
Health Fusion & Fault Confidence
Local State Decision

## Slide 6
System Block Diagram
SENSOR HEALTH
SHT31 • Temperature / humidity EWMA / CUSUM • Range • Drift
ELECTRICAL HEALTH
INA226 • Voltage / Current / Power Shunt resistor • Voltage divider
CONTROLLER HEALTH
MCU temperature • Resets Watchdog status • Communication errors
FAULT INJECTION RIG
Digital potentiometer • MOSFETs / relays Sensor & electrical fault simulation
STM32F446RE MICROCONTROLLER
FEATURE EXTRACTION
Mean • Variance • Slope • RMS • EWMA • CUSUM • Cross-correlation
TINYML INFERENCE
Autoencoder + Random Forest • int8 quantization • TensorFlow Lite Micro
HEALTH FUSION
Multi-parameter weighted fusion • Confidence score (0–100%)
STATE MACHINE
Normal → Warning → Degraded → Critical
EXTERNAL HARDWARE WATCHDOG
TPS3813K33 Independent hardware reset if firmware hangs Connection: NRST
DISPLAY
OLED • Status LEDs Normal / Warning / Fault
LOCAL RESPONSE
Relay trip • Fault isolation Safe fallback mode
DATA LOGGING
MicroSD • W25Q64 SPI Flash RTC timestamps • Event / fault logs
COMMUNICATION
MAX13487EESA • RS485 / Modbus RTU Fleet aggregation (target up to 1200 m)
POWER MANAGEMENT
12V input → LM2596 buck (12V → 5V) → AMS1117 LDO (5V → 3.3V)
Powers MCU, sensors, ccommunication and peripherals

## Slide 7
Target Specifications & Hardware Selection
Parameter | Target Specification | Rationale
Inference Latency | < 100 ms | Ensures real-time detection before critical damage.
Flash Budget | < 80 KB (of 512 KB) | Proves viability on a cost-sensitive, resource-aware MCU.
RAM Budget | < 32 KB (of 128 KB) | Leaves headroom for other application tasks.
Current Draw | < 20 mW incremental | Maintains energy efficiency for remote edge deployments.
Fault States | 4-State Model | Enables graceful degradation (Normal → Critical).
Comms Range | Up to 1200m | Ensures fleet aggregation in large factories without Wi-Fi.
Architecture Rationale:-
STM32F446RE DSP support enables on-device TinyML without an external NPU. I²C reduces sensor pin count; isolated RS485 supports long-distance communication in electrically noisy environments. The TPS3813 watchdog remains independent of firmware to recover from lockups.
Subsystem | Selected Hardware | Interface / Protocol
Core Controller | STM32F446RE (Arm Cortex-M4, 180 MHz) | —
Sensor Health | SHT31-DIS (Temperature & Humidity) | I2C (400 kHz)
Electrical Health | INA226 (Voltage, Current, Power) | I2C (400 kHz)
Fleet Comms | MAX13487EESA (Isolated RS485) | Modbus RTU (UART)
Local Logging | W25Q64 SPI Flash & MicroSD Card | SPI
Safety / Watchdog | TPS3813K33 (External Hardware Watchdog) | GPIO / NRST
Actuation | 5V SPDT Relay & ULN2003 Driver | GPIO
Power Management | LM2596 (Buck) & AMS1117 (LDO) | 12V → 5V → 3.3V

## Slide 8
Figure: Custom 120x100mm 2-layer PCB integrating sensing, communication, and fault-injection circuitry for cost-sensitive viability.
3D Design View
03 / 06
120 × 100
mm board footprint
2-layer
FR-4 PCB
1.6 mm
board thickness
FUNCTIONAL ZONES REPRESENTED IN THE LAYOUT
DESIGN INTENT
A compact, low-cost board integrates monitoring, communications and deliberate fault stimulus on one controller platform.
Physical Specifications
Functional Zone | Description
CORE COMPUTE | STM32F446RE MCU and 8 MHz crystal clock.
SENSING & COMMS | I²C sensor path plus isolated RS485 fleet interface.
RESILIENCE | External watchdog, protection devices and fault-injection circuitry.
DATA & POWER | W25Q64 SPI flash, microSD interface, LM2596 buck and AMS1117 LDO.
PCB

## Slide 9
KiCAD Schematic
Design Rationale:-
The schematic integrates independent health-monitoring mechanisms (I2C sensors, RS485, Watchdog) around a single low-cost STM32F446RE MCU. The dedicated fault-injection module allows us to physically induce and test faults on the running device, proving the system's autonomous response.
Electronics Schematic & PCB Integration
SCHEMATIC SUBSYSTEM MAP
Subsystem | Description
MCU + CLOCK | STM32F446RE with 8 MHz crystal and debug header.
SENSORS + I²C | SHT31-DIS and INA226 share the internal sensor bus.
FLEET COMMUNICATION | MAX13487EESA isolated RS485 interface for Modbus RTU.
LOCAL DATA | W25Q64 SPI flash and microSD card interface.
SAFETY + FAULTS | TPS3813 watchdog, reset path, protection and fault-injection header.
POWER RAILS | 12 V input conversion to 5 V and 3.3 V rails.

## Slide 10
Bill of Materials
05 / 06
PROCUREMENT STATUS
Core parts are listed as locally or domestically sourced within India; the maximum stated shipping lead time is 7 business days.
COST-SENSITIVE VIABILITY
Under the ₹4,200 target in the supplied project narrative, keeping electronics costs accessible for MSME retrofits.
Component | Part / Specification | Quantity | Lead Time | Estimated Cost (INR)
Core Controller | STM32F446RET6 (Arm Cortex-M4, 180MHz) | 1 | Local (3 days) | ₹550
Health Sensors | SHT31-DIS (Temp/Humidity) & INA226 (Power) | 1 Set | Domestic (7 days) | ₹700
Comms & RTC | MAX13487EESA (RS485) & DS3231SN (RTC) | 1 Set | Domestic (5 days) | ₹380
Data Logging | W25Q64 (8MB SPI Flash) & MicroSD Slot | 1 Set | Local (2 days) | ₹130
Power & Relay | LM2596, AMS1117, 5V Relay, ULN2003 | 1 Set | Local (2 days) | ₹250
Fault Injection | TPS3813 Watchdog, MOSFETs, TVS Diodes | 1 Set | Domestic (5 days) | ₹350
Passives | 8MHz Crystal, Capacitors, Resistors, LEDs | 1 Set | Local (2 days) | ₹250
Custom PCB | FR4 2-Layer 1.6mm (120x100 mm) | 5 | Domestic (6 days) | ₹1,500

## Slide 11
Maker Journey
Figure: Team reviewing electronic design and development work together
Stage 1 to Stage 2 Engineering Progress & Evidence
SYSTEM & FIRMWARE
STM32F446RE-based edge controller; firmware assets organized in the repository.
ELECTRONICS DESIGN
KiCad schematic, PCB layout and bill of materials are grouped under /hardware.
TINYML WORKFLOW
ML data, notebooks and model assets are organized under /ml.
DOCUMENTATION & DEMO
Architecture, validation documents, presentation material and demo-video links are grouped in the repository.

## Slide 12
RAW REPOSITORY LINK
github.com/ConquerToFreedom/SwasthEdge
Firmware • Hardware • ML • Documentation • Presentation • Demo resources
Work-In-Progress Software Evidence
Figure - EDA layout software (KiCad)

## Slide 13
Safety & Hazard Mitigation
Standards / Compliance
Standards are considered as design and validation references; no formal compliance or certification is claimed at the prototype stage.
Fault Confirmation Use sensor readings together with voltage, current and MCU-health indicators before increasing fault confidence.
Graceful Degradation Normal → Warning → Degraded → Critical operating states prevent unnecessary escalation.
Local Fail-Critical Response Warning, faulty-sensor isolation, fallback values, reduced operation, communication recovery, or predefined critical state.
Fault Monitoring Monitor sensor drift, power abnormalities, controller health and communication failures continuously.
Functional Safety —
IEC 61508
Reference for safety-related electrical/electronic/programmable functions and their safety lifecycle.
Industrial EMC —
IEC 61000-6-2 / IEC 61000-6-4
Reference for industrial-environment immunity and emissions of electrical/electronic equipment.
Industrial Cybersecurity —
IEC 62443-4-1 / IEC 62443-4-2
Reference for secure product development and technical security requirements for industrial automation/control-system components.

## Slide 14
October 2026 — System Setup & Breadboard Prototype
Finalize MCU, sensor and power-monitoring architecture
Establish normal sensor/controller behaviour
Build breadboard-based functional prototype
Integrate voltage/current and sensor monitoring
Prepare controlled fault-injection setup
November 2026 — Self-Diagnosis Firmware
Implement sensor-drift detection using EWMA/CUSUM
Implement MCU health and communication monitoring
Integrate local diagnostic logging
Evaluate lightweight TinyML-based anomaly detection
Prepare firmware for PCB migration
December 2026 — PCB & Health-Fusion Integration
Finalize schematic and PCB layout
Develop health-fusion and fault-confidence logic
Implement Normal → Warning → Degraded → Critical states
Integrate local fault responses and fallback handling
Assemble and bench-test PCB prototype
January 2027 — Validation & Stage 3 Readiness
Conduct controlled fault-injection tests
Compare sensor-only vs. multi-parameter health fusion
Measure detection performance, false alarms, latency, CPU/RAM and power overhead
Validate PCB prototype and Stage 3 field-testing readiness
Roadmap
Stage 3 Target: Working SwasthEdge prototype validated through controlled fault injection and ready for functional field testing.
Fabrication Phase (Months 1 - 2)
Integration & Field Demo (Months 3 - 4)

## Slide 15
Technical Challenges & Risks
Engineering Challenge / Risk | Potential Impact
Distinguishing Drift from Normal Variation | Temporary fluctuations may be misclassified as persistent sensor faults, causing false alarms.
Multi-Parameter Health Fusion | Combining sensor, power, and MCU-health indicators while maintaining reliable fault confidence can increase algorithm complexity.
Limited MCU Resources | EWMA/CUSUM, health-fusion logic, logging and continuous monitoring must remain within available CPU, RAM, flash and power budgets.
Abnormal Power / Supply Conditions | Voltage or current disturbances may affect both the monitored sensor and controller, making fault attribution difficult.
Communication Loss | Network failure can interrupt remote monitoring and requires reliable local diagnostic logging and recovery logic.
Graceful Degradation Decisions | Selecting the correct transition between Normal → Warning → Degraded → Critical without unnecessary shutdown is a key control challenge.
Key Engineering Constraint: Achieve reliable local self-diagnosis while keeping computation, memory, latency and additional power consumption suitable for a low-cost MCU.

## Slide 16
Potential Risk / Failure | Potential Solution / Mitigation
Sensor Drift | Detect gradual deviation using EWMA/CUSUM and validate against other health indicators.
Sensor Disconnection / Failure | Identify abnormal readings or loss of data, isolate the faulty sensor, and use a fallback value where applicable.
Power Instability / Abnormal Current | Continuously monitor voltage and current and raise fault confidence when electrical behaviour becomes abnormal.
MCU / Controller Fault | Monitor temperature, reset cause, watchdog, communication and memory health; move to a predefined safe state when required.
Communication Failure / Network Loss | Attempt communication recovery and use local diagnostic logging so fault information is retained without network connectivity.
Persistent vs. Temporary Abnormality | Use health fusion + fault-confidence rather than relying on a single threshold.
Escalating Fault / Unsafe Operation | Apply graceful degradation: Normal → Warning → Degraded → Critical.
Potential Solutions & Risk Mitigation
Fallback strategy: When the primary signal or subsystem becomes unreliable, SwasthEdge progressively reduces risk through validation, isolation, fallback operation, recovery attempts, and safe-state transition.

## Slide 17
https://drive.google.com/file/d/18aVEA84JQQvSDFFv31FtURB8URP6s71-/view?usp=sharing
Source: kicad.org
https://drive.google.com/file/d/1UwEtkNEv0FDomdyTmOcfXZVLesxRijE1/view?usp=sharing
Source: kicad.org
References & Sources
https://drive.google.com/file/d/1wYRzzO_YdnxeIhUycdN4n_Zos5l7g55y/view?usp=sharing
Source: kicad.org

## Slide 18
Image Sources
Source: drive.google.com
https://drive.google.com/file/d/1MzbbyO2kHNY1_z6F4SUou90y5NS2iWfl/view?usp=drivesdk